## Slide 1: intro2PCBdesign – lab64
bad boards

## Slide 2: board1

## Slide 3: board1
Trace loops
  EMI disaster

## Slide 4: board1
Trace loops
  EMI disaster
  Loops of wires creates an antenna; aka “Loop antenna”

## Slide 5: board1
Trace loops
  EMI disaster
  Loops of wires creates an antenna; aka “Loop antenna”
Acute trace angles
  Induced coupling between traces

## Slide 6: board1
Trace loops
  EMI disaster
  Loops of wires creates an antenna; aka “Loop antenna”
Acute trace angles
  Induced coupling between traces
    Induces noise in those traces

## Slide 7: board1
Trace loops
  EMI disaster
  Loops of wires creates an antenna; aka “Loop antenna”
Acute trace angles
  Induced coupling between traces
    Induces noise in those traces
These faults will destroy any high frequency projects.

## Slide 8: board2

## Slide 9: board2
Different widths on the same trace

## Slide 10: board2
Different widths on the same trace
  Different impedances on same trace

## Slide 11: board2
Different widths on the same trace
  Different impedances on same trace
    Reflections in high frequency signals
      Byebye signal

## Slide 12: board2
Different widths on the same trace
  Different impedances on same trace
    Reflections in high frequency signals
      Byebye signal
Acute angles

## Slide 13: board2
Different widths on the same trace
  Different impedances on same trace
    Reflections in high frequency signals
      Byebye signal
Acute angles
IPC-2152 - Standard for Determining Current-carrying Capacity in Printed Board Design
IPC – “The global trade association serving the printed board and electronics assembly industries, their customers and suppliers”
http://www.ipc.org/

## Slide 14: board3

## Slide 15: board3
Different signal, but parallel traces

## Slide 16: board3
Different signal, but parallel traces
  Induces coupling
    Induces noise
Adjacent signal layers

## Slide 17: board3
Different signal, but parallel traces
  Induces coupling
    Induces noise
Adjacent signal layers
  No ground plane in between can induce noise
    Ground bounce (where is ground?)

## Slide 18: board3
Different signal, but parallel traces
  Induces coupling
    Induces noise
Adjacent signal layers
  No ground plane in between can induce noise
    Ground bounce (where is ground?)
Bad component placement makes bad trace routing seem like a good idea

## Slide 19: board4

## Slide 20: board4
Mismatched lengths for a critical signal

## Slide 21: board4
Mismatched lengths for a critical signal
  Different lengths means different arrival times

## Slide 22: board4
Mismatched lengths for a critical signal
  Different lengths means different arrival times
Outer trace = 1.6105 in
Inner trace = 1.2625 in
Difference = 0.348 in
Dielectric Constant FR-4 dielectric ~= 4
Speed of EM signal in a vacuum ~= 11.8in/ns
Very rough estimate:
  Td = 0.348 in / (11.8 in/ns / sqrt(Ereff)) =50ps delay in propagation
https://blog.zuken.com/how-to-calculate-trace-length-from-time-delay-value-for-high-speed-signals/

## Slide 23: board4
Mismatched lengths for a critical signal
  Different lengths means different arrival times
Outer trace = 1.6105 in
Inner trace = 1.2625 in
Difference = 0.348 in
Dielectric Constant FR-4 dielectric ~= 4
Speed of EM signal in a vacuum ~= 11.8in/ns
Very rough estimate:
  Td = 0.348 in / (11.8 in/ns / sqrt(Ereff)) =50ps delay in propagation
  Rise times for modern digital signals are faster than this!
https://blog.zuken.com/how-to-calculate-trace-length-from-time-delay-value-for-high-speed-signals/

## Slide 24: parting thoughts
A lot can go wrong when making a PCB

## Slide 25: parting thoughts
A lot can go wrong when making a PCB
  Poor layout
  Mistakes in fabrication
    Mistakes in assembly

## Slide 26: parting thoughts
A lot can go wrong when making a PCB
  Poor layout
  Mistakes in fabrication
    Mistakes in assembly
Defensive driving exists for good reason – defend against risks
  Same idea – layout PCBs with a defensive mindset

## Slide 27: overflow

## Slide 28: overflow